## Slide 1
2021.09.16
Speaker: Dohun Kwon
Kyung Hee University
Department of Nuclear Engineering
Contact: skdmlclsrn11@gmail.com
Development and Applications of
DICE(Dynamic Integrated Consequence Evaluation)
2021 Korean Institute of Hazardous Materials

## Slide 2: Table
Background
Method of Development
Mode
Summary
Application

## Slide 3: Background
PSA(Probabilistic Safety Assessment)
Methodology for using complex engineering system (ex. Nuclear power plant, Aerospace, etc.)
PSA = Fault Tree + Event Tree
  Fault Tree(FT): Analysis method for a state in which the system cannot perform the necessary functions
  Event Tree(ET): Analysis method for important event sequence about the selected initiating event
Success
Fail
Event Tree
Falut Tree

## Slide 4: Background
Limitation for conventional PSA
Difficulty for consider dynamically nonlinear processes
Temporal dependency
Human error such as Errors of Omission(EOO), Errors of Commissions (EOC)
IDPSA(Integrated Deterministic-Probabilistic Safety Assessment)
  … is a methodology that analyzes the metric related to the safety of the system by reflecting probabilistic (or stochastic) situational changes in the deterministic simulation process of a physical model.
OVERCOME

## Slide 5: Method of Development
Dynamic analysis of external events
Error of commission
Malicious threats
Procedure’s coverage
Microscopic analysis of a specific sequence:
Design basis / Severe accidents
Interconnected systems’ behavior
Super-fast event predictor
Signal Malfunctions
Cyber attacks
Stochastic recovery tasks:
Figure. Architecture and Applications of DICE

## Slide 6
Method of Development (1/4)
Schematic diagram of DICE for Level 1 and Level 2
Structure
  DDET (Discrete Dynamic Event Tree) scheduler in multi-machine/multi-core running environment
Example of DDET mechanism

## Slide 7
Structure
  Physical module
    Connected with a simulation code or a digital twin model
    MARS-KS (Korean regulatory safety analysis code)
    Receives monitoring variables from a simulation
    Supplies control variables to a simulation
Schematic diagram of DICE for Level 1 and Level 2
Method of Development (2/4)

## Slide 8
Structure
  Diagnosis module
    Auto sub-module
      Logical statements for systems’ variables
      Ex) Actuation of RPS(Reactor Protection System) or ESFAS(Engineered Safety Feature Actuation System)
    Manual sub-module
      Human model
    Receives monitoring variables
    Decides & Supplies branching points
Schematic diagram of DICE for Level 1 and Level 2
Method of Development (3/4)

## Slide 9
Structure
  Reliability module
    Stochastic fault & recovery model
    Receives branching decisions
    Supplies branching probabilities / control variables
Schematic diagram of DICE for Level 1 and Level 2
Method of Development (4/4)

## Slide 10: Mode(1/2, Mode 1: Multi-branch)
Minimum number of simulations for MECE Spectrum
(Equipment failure check at only a branching point)
Easy tree-structured visualization
Cutset creation and quantification process required
Still deterministic
Capture for Interpolating censored risk
dt
Simulation
Starts
dt
dt
dt
Auto Task
Module ?
dt
dt
dt
dt
dt
dt
Manual Task
Module ?
Single Fail?
Double Fail?
All Fail?
In an hour?
In two hour?
In a day?
Damage!
Damage!
OK?
OK!
Damage?
OK!
Diagnosis Module
(Auto Action)
Diagnosis Module
(Manual Action)
Scheduler
Physical Module
Reliability Module
Reliability Module

## Slide 11: Mode(2/2, Mode 2: Single-branch)
Vast amount of simulations for unknown scenarios
(Equipment failure check at everytime)
Difficulty in visualization
Simple quantification
Full stochastic
Capture for extrapolating censored risk
dt
Simulation
Starts
dt
dt
dt
Auto Task
Module ?
dt
dt
dt
dt
dt
dt
Manual Task
Module ?
Single Fail?
Double Fail!
All Fail?
In an hour?
In two hour?
at 1:00!
OK? or Damage?
Diagnosis Module
(Auto Action)
Diagnosis Module
(Manual Action)
Scheduler
Physical Module
Reliability Module
Reliability Module
Reliability Module
Reliability Module

## Slide 12: Future research
  Mode 1 Applications
    Evaluation of the coverage of operating procedures
    Detailed analysis of specific sequence
    Analysis of maintenance or recovery
  Mode 2 Applications
    Analysis of unexpected tasks
    Analysis of interconnected multiple facilities
    Analysis of dependency between human error and time temporal

## Slide 13: Application
SBLOCA for Reference Model
A: Auto sub-module
M: Manual sub-module
A_1_2: RPS Success
A_2_4: Three HPSI Success
A_3_2: Three LPSI Success A_4_4: Three HPRC Success A_6_2: AFW Failed
M_2_6: RCP Trip
M_4_6: CSP Trip
M_5_5: RHRP Trip
M_10_5: F&B Success
M_15_6: RHRP Operation

## Slide 14
Thank you for attention
Email: skdmlclsrn11@gmail.com